## Slide 1
Microprocessors & Computer Architecture
UE18CS253
UNIT -1
Session – 3 & 4
ARM
Assembly Language Programming
1
Credits:
MPCA Team
SESSION JAN-MAY 2020
Notes: 1

## Slide 2
The ARM
2
Instruction Set
SESSION JAN-MAY 2020

## Slide 3
ARM Assembly Language Programming
ARM instructions are grouped as follows.
Data Processing Instructions.
Ex: MOV, ADD, SUB , CMP, CMN, etc.,
Branch Instructions.
Ex: B , BL, BGT, BLT, BGE, BLE, etc.,
Data Transfer Instructions.
Ex: LOAD – STORE Instructions- LDR, STR, LDM, STM, etc.,
Software Interrupt Instructions.
Ex: SWI Ox11, etc.,
Program Status Register Instructions.
Ex: MSR , MRS, etc.,
3
SESSION JAN-MAY 2020

## Slide 4
ARM Instruction Set
Data Processing Instructions.
MOVE instruction
Syntax: <mnemonic><cond><s> <dest Rd>, <src op1 Rn>
Ex1: MOV RO, R1
Moves the contents of the source operand register R1 and copies to the destination register R0.
Ex2: MVN R0, R1
Moves the complemented value of the source operand register R1 and stores to the destination register R0.
4
SESSION JAN-MAY 2020
Notes: 4

## Slide 5
ARM Instruction Set
Arithmetic Instruction:
Syntax: <mnemonic><cond><s> <dest Rd>,<src op1 Rn >,<src op2 Rm>
Ex3: ADD R3, R1, R2 : R3 = R1 + R2
Adds the contents of the source operand registers R1 & R2 and stores the result in the destination register R3.
Compare Instruction:
Syntax: <mnemonic><cond><s> <dest Rd>, <src op1 Rn >,
Ex4: CMP R3, R1
Neither source nor destination fields are affected.
Ex5: CMN R3, R1
Performs the operation R3 + R1 and sets the condition codes / flags.
Neither source nor destination fields are affected.
5
SESSION JAN-MAY 2020

## Slide 6
Setting the condition codes
Any data processing instruction can set the condition codes if the programmers wish it to
64-bit addition
ADDS R2, R2, R0
ADC R3, R3, R1
R1
R0
R3
R2
R3
R2
+
6
SESSION JAN-MAY 2020

## Slide 7
Comparison
CMP R1, R2 @ set cc on R1-R2
CMN R1, R2 @ set cc on R1+R2
TST R1, R2 @ set cc on R1 and R2
TEQ R1, R2 @ set cc on R1 xor R2
compare
compare negated
bit test
test equal
7
SESSION JAN-MAY 2020
CODE

## Slide 8
ARITHMETIC OPERATIONS
MOV R4, #10
MVN R5, R4
MOV R1, #5
MOV R2, #2
ADD r0, r1, r2 ;r0:=r1+r2
ADC r0, r1, r2 ;r0:=r1+r2+C
SUB r0, r1, r2 ;r0:=r1–r2
SBC r0, r1, r2 ;r0:=r1–r2+C–1
RSB r0, r1, r2 ;r0:=r2–r1, Reverse Subtraction
RSC r0, r1, r2 ;r0:=r2–r1+C–1
By default data processing operations do not affect the condition flags
8
SESSION JAN-MAY 2020
CODE

## Slide 9
Bit-wise Logical Operations
AND r0, r1, r2 ;r0 := r1 AND r2
ORR r0, r1, r2 ;r0 := r1 OR r2
EOR r0, r1, r2 ;r0 := r1 XOR r2
BIC r0, r1, r2 ;r0 := r1 AND (NOT r2), bit clear
9
SESSION JAN-MAY 2020
CODE

## Slide 10
Shifted register operands
One operand to ALU is routed through the Barrel shifter. Thus, the operand can be modified before it is used. Useful for fast multiplication and dealing with lists, table and other complex data structure. (similar to the displacement addressing mode in CISC.)
Some instructions (e.g. MUL, CLZ, QADD) do not read barrel shifter.
10
SESSION JAN-MAY 2020
Notes: 10

## Slide 11
Barrel Shifter - Block Diagram
11
SESSION JAN-MAY 2020

## Slide 12
Barrel Shifter
ARM architecture supports instructions which performs a shift with ALU operation.
The shifter performance is therefore critical as it contributes directly to the datapath cycle time.
To minimize the delay through the shifter, A cross-bar switch matrix is used to steer each input to appropriate output.
Example shown is 4 x 4 matrix cross bar switch.
ARM uses a 32 x 32 matrix cross bar switch.
Each input is connected to each output through a switch.
12
SESSION JAN-MAY 2020

## Slide 13
Barrel Shifter - Function
Shift Operation – Left
  One left shift diagonal line is turned on.
Shift Operation – Right
  One right shift diagonal line is turned on.
Arithmetic Shift right
  Uses sign extension rather than zero filling for unconnected output.
Rotate operation
13
SESSION JAN-MAY 2020
The right shift diagonal is enabled together with complementary left shift diagonal.

## Slide 14
Multiplication by constant using the barrel shifter
Multiplication by 2^n (1,2,4,8,16,32..)
MOV Ra, Rb, LSL #n
Multiplication by 2^n+1 (3,5,9,17..)
ADD Ra,Ra,Ra,LSL #n
Multiplication by 2^n-1 (3,7,15..)
RSB Ra,Ra,Ra,LSL #n
Multiplication by 6
ADD Ra,Ra,Ra,LSL #1 ; multiply by 3
MOV Ra,Ra,LSL#1 ; and then by 2
Multiply by 10 and add in extra number
ADD Ra,Ra,Ra,LSL#2 ; multiply by 5
ADD Ra,Rc,Ra,LSL#1 ; multiply by 2 and add in next digit
14
SESSION JAN-MAY 2020
CODE

## Slide 15
Barrel Shifter - Examples
Shift Operation – Left: One left shift diagonal line is turned on.
Example 1: ADD R0, R1, R2, LSL #3
  Since LSL is used, it selects left diagonal #3.
Rotate operation: The right shift diagonal is enabled together with complementary left shift diagonal.
Example 2: ADD R0, R1, R2, ROR #3
Selects Right diagonal #3 and left diagonal # 29.
15
SESSION JAN-MAY 2020
Notes: 15

## Slide 16
Logical shift left
MOV R0, R2, LSL #2 @ R0:=R2<<2
@ R2 unchanged
Example: 0…0 0011 0000
Before R2=0x00000030
After R0=0x000000C0
R2=0x00000030
C
0
register
16
SESSION JAN-MAY 2020
Notes: 16

## Slide 17
Logical shift right
MOV R0, R2, LSR #2 @ R0:=R2>>2
@ R2 unchanged
Example: 0…0 0011 0000
Before R2=0x00000030
After R0=0x0000000C
R2=0x00000030
C
0
register
17
SESSION JAN-MAY 2020
Notes: 17

## Slide 18
Arithmetic shift right
MOV R0, R2, ASR #2 @ R0:=R2>>2
@ R2 unchanged
Example: 1010 0…0 0011 0000
Before R2=0xA0000030
After R0=0xE800000C
R2=0xA0000030
MSB
register
C
18
SESSION JAN-MAY 2020
Notes: 18

## Slide 19
Rotate right
MOV R0, R2, ROR #2 @ R0:=R2 rotate
@ R2 unchanged
Example: 0…0 0011 0001
Before R2=0x00000031
After R0=0x4000000C
R2=0x00000031
register
19
SESSION JAN-MAY 2020
Notes: 19

## Slide 20
Rotate right extended
MOV R0, R2, RRX @ R0:=R2 rotate
@ R2 unchanged
Example: 0…0 0011 0001
Before R2=0x00000031, C=1
After R0=0x80000018, C=1
R2=0x00000031
register
C
C
20
SESSION JAN-MAY 2020
Notes: 20

## Slide 21
Shifted register operands
21
SESSION JAN-MAY 2020
Notes: 21

## Slide 22
Shifted register operands
22
SESSION JAN-MAY 2020
Notes: 22

## Slide 23
Shifted register operands
It is possible to use a register to specify the number of bits to be shifted; only the bottom 8 bits of the register are significant.
@ array index calculation
ADD R0, R1, R2, LSL R3 @ R0:=R1+R2*2R3
@ fast multiply R2=35xR0
ADD R0, R0, R0, LSL #2 @ R0’=5xR0
RSB R2, R0, R0, LSL #3 @ R2 =7xR0’
23
SESSION JAN-MAY 2020

## Slide 24
Shifted register operands
24
SESSION JAN-MAY 2020

## Slide 25
Multiplication as Addition & Subtraction
MOV R1, #35
MUL R2, R0, R1
or
ADD R0, R0, R0, LSL #2 @ R0’=5xR0
RSB R2, R0, R0, LSL #3 @ R2 =7xR0’
25
SESSION JAN-MAY 2020
CODE

## Slide 26
ARM Instruction Set
Using the ARM instruction set, write Assembly level language instructions / sequence /programs
to perform the following as directed.
Compile the following C assignment statements into ARM.
  A = B + C;
  D = A – C;
  Perform D = A - C using RSB instruction.
Convert the following assignment into ARM.
  F = ( G + H ) – ( I + J ).
use the register R0 to R4 as operands F to J respectively.
Convert the statement into ARM where the operand is in memory.
  G = H + A [ 10 ].
Assignment.
Note: User different addressing modes both at source & destination operand positions.
26
SESSION JAN-MAY 2020

## Slide 27
Q & A on Arm Instruction Set – data processing group
27
SESSION JAN-MAY 2020