## Slide 1
Microprocessor & Computer Architecture
UE18CS253
Session – 4 & 5
ARM
Assembly Language Programming
1
Credits:
MPCA Team
SESSION JAN-MAY 2020
Notes: 1

## Slide 2
The ARM
2
Flow control Instructions
SESSION JAN-MAY 2020

## Slide 3
Flow control instructions
Determine the instruction to be executed next
pc-relative offset within 32MB
3
SESSION JAN-MAY 2020
Notes: 3

## Slide 4
Flow control instructions
Branch instruction
B label
…
label: …
Conditional branches
MOV R0, #0
loop: …
ADD R0, R0, #1
CMP R0, #10
BNE loop
4
SESSION JAN-MAY 2020

## Slide 5
Branch conditions
5
SESSION JAN-MAY 2020

## Slide 6
Branches
6
SESSION JAN-MAY 2020

## Slide 7
Branch and link
BL instruction save the return address to R14 (lr)
BL sub @ call sub
CMP R1, #5 @ return to here
MOVEQ R1, #0
…
sub: … @ sub entry point
…
MOV PC, LR @ return
7
SESSION JAN-MAY 2020

## Slide 8
The ARM
8
Data Transfer Instruction Set
SESSION JAN-MAY 2020

## Slide 9
Data transfer instructions
Move data between registers and memory
Basic forms
  Single register load/store
    Ex: LDR , STR
  Multiple register load/store
    Ex: LDM, STM
9
SESSION JAN-MAY 2020

## Slide 10
Single register load/store
10
SESSION JAN-MAY 2020
CODE

## Slide 11
Single register load/store
No STRSB/STRSH since STRB/STRH stores both
signed/unsigned ones
11
SESSION JAN-MAY 2020
CODE

## Slide 12
Single register load/store
The data items can be a 8-bit byte, 16-bit half-word or 32-bit word. Addresses must be boundary aligned. (e.g. 4’s multiple for LDR/STR)
LDR R0, [R1] @ R0 := mem32[R1]
STR R0, [R1] @ mem32[R1] := R0
LDR, LDRH, LDRB for 32, 16, 8 bits
STR, STRH, STRB for 32, 16, 8 bits
12
SESSION JAN-MAY 2020
CODE

## Slide 13
Addressing modes
Memory is addressed by a register and an offset.
LDR R0, [R1] @ mem[R1]
Three ways to specify offsets:
  Immediate
LDR R0, [R1, #4] @ mem[R1+4]
  Register
LDR R0, [R1, R2] @ mem[R1+R2]
  Scaled register
  @ mem[R1+4*R2]
LDR R0, [R1, R2, LSL #2]
13
SESSION JAN-MAY 2020
CODE
Notes: 13

## Slide 14
Addressing modes
Pre-index addressing (LDR R0, [R1, #4]) without a writeback
Auto-indexing addressing (LDR R0, [R1, #4]!)
Pre-index with writeback calculation before accessing with a writeback
Post-index addressing (LDR R0, [R1], #4)
calculation after accessing with a writeback
14
SESSION JAN-MAY 2020
Notes: 14

## Slide 15
Pre-index addressing
LDR R0, [R1, #4] @ R0=mem[R1+4]
@ R1 unchanged
R0
R1
+
LDR R0, [R1, ]
15
SESSION JAN-MAY 2020
Notes: 15

## Slide 16
Auto-indexing addressing
LDR R0, [R1, #4]! @ R0=mem[R1+4]
@ R1=R1+4
LDR R0, [R1, ]!
R0
R1
+
No extra time; Fast;
16
SESSION JAN-MAY 2020
Notes: 16

## Slide 17
Post-index addressing
LDR R0, [R1], #4 @ R0=mem[R1]
@ R1=R1+4
R0
R1
+
LDR R0,[R1],
17
SESSION JAN-MAY 2020
Notes: 17

## Slide 18
Comparisons
Pre-indexed addressing
LDR R0, [R1, R2] @ R0=mem[R1+R2]
@ R1 unchanged
Auto-indexing addressing
LDR R0, [R1, R2]! @ R0=mem[R1+R2]
@ R1=R1+R2
Post-indexed addressing
LDR R0, [R1], R2 @ R0=mem[R1]
@ R1=R1+R2
18
SESSION JAN-MAY 2020
Notes: 18

## Slide 19
Example
19
SESSION JAN-MAY 2020

## Slide 20
Example
20
SESSION JAN-MAY 2020
Notes: 20

## Slide 21
Example
21
SESSION JAN-MAY 2020

## Slide 22
Summary of addressing modes
22
SESSION JAN-MAY 2020

## Slide 23
Summary of addressing modes
23
SESSION JAN-MAY 2020

## Slide 24
Summary of addressing modes
24
SESSION JAN-MAY 2020

## Slide 25
Summary of addressing modes
25
SESSION JAN-MAY 2020

## Slide 26
Load an address into a register
Note that all addressing modes are register-offsetted. Can we issue LDR R0, Table? The pseudo instruction ADR loads a register with an address
table: .word 10
…
LDR R0, table
Assembler transfer pseudo instruction into a sequence of appropriate instructions
sub r0, pc, #12
26
SESSION JAN-MAY 2020

## Slide 27
Application
ADR R1, table
loop: LDR R0, [R1]
ADD R1, R1, #4
@ operations on R0
…
ADR R1, table
loop: LDR R0, [R1], #4
@ operations on R0
…
table
R1
27
SESSION JAN-MAY 2020

## Slide 28
Q & A on Arm Instruction Set – Data Transfer group
28
SESSION JAN-MAY 2020