## Slide 1
UE18CS253
Unit-1
Session – 6
ARM
Assembly Language Programming
1
Microprocessors & Computer Architecture
Credits:
MPCA Team
SESSION JAN-MAY 2020
Notes: 1

## Slide 2
The ARM
2
Multiplication Instructions
SESSION JAN-MAY 2020

## Slide 3
Multiplication
MUL R0, R1, R2
  @ R0 = (R1xR2)[31:0]
Features:
  Second operand can’t be immediate
  The result register must be different from the first operand
  Cycles depends on core type
  If S bit is set, C flag is meaningless
3
SESSION JAN-MAY 2020

## Slide 4
Multiplication
Multiply-accumulate (2D array indexing)
MLA R4, R3, R2, R1 @ R4 = R3xR2+R1
Multiply with a constant can often be more efficiently implemented using shifted register operand.
MOV R1, #35
MUL R2, R0, R1
or
ADD R0, R0, R0, LSL #2 @ R0’=5xR0
RSB R2, R0, R0, LSL #3 @ R2 =7xR0’
4
SESSION JAN-MAY 2020

## Slide 5
MLA Example:
Matrix Representation in memory
Row Major Order for a 3 x 3 matrix :
A [ 2, 2] = Row Num. x No. of elements per row + Column Num.
2 x 3 + 2 = 8th location.
Since each location is of 4 bytes, the address of the 3rd element in the 2nd row is 8 x 4 = 32.
This is achieved in ARM processor, using MLA instruction as follows.
MLA R1, R2, R3, R4
Mnemonic
R1: Dst ; R2: Row #
R3: # of elements per row ; R4: col #
To get consecutive data elements in a @D Array.
1
2
7
4
6
3
5
8
9
00000000
00000001
00000020
5
SESSION JAN-MAY 2020
CODE

## Slide 6
Multiplication
6
SESSION JAN-MAY 2020
CODE

## Slide 7
Multiplication – Example 1
7
SESSION JAN-MAY 2020

## Slide 8
Multiplication Example 2
8
SESSION JAN-MAY 2020

## Slide 9
The ARM
9
Conditional Execution
SESSION JAN-MAY 2020

## Slide 10
Conditional Execution
Almost all ARM instructions have a condition field which allows it to be executed conditionally.
MOVCS R0, R1
10
SESSION JAN-MAY 2020
CODE
Notes: 10

## Slide 11
Conditional Execution
CMP R0, #5
BEQ bypass @ if (R0!=5) {
ADD R1, R1, R0 @ R1=R1+R0-R2
SUB R1, R1, R2 @ }
bypass: …
Rule of thumb: if the conditional sequence is three instructions
or less, it is better to use conditional execution than a branch.
; smaller and faster
CMP R0, #5
ADDNE R1, R1, R0
SUBNE R1, R1, R2
11
SESSION JAN-MAY 2020

## Slide 12
Conditional Execution
if ((R0==R1) && (R2==R3)) R4++
CMP R0, R1
BNE skip
CMP R2, R3
BNE skip
ADD R4, R4, #1
skip: …
CMP R0, R1
CMPEQ R2, R3
ADDEQ R4, R4, #1
12
SESSION JAN-MAY 2020

## Slide 13
The ARM
13
Multiple Load / Store Instructions
SESSION JAN-MAY 2020

## Slide 14
Multiple register load/store
Transfer a block of data more efficiently.
Used for procedure entry and exit for saving and restoring workspace registers and the return address
For ARM7, 2+Nt cycles
(N: #words, t: time for a word for sequential access).
Increase interrupt latency since it can’t be
interrupted.
registers are arranged an in increasing order;
LDMIA R1, {R0, R2, R5} @ R0 = mem[R1]
@ R2 = mem[R1+4]
@ R5 = mem[R1+8]
14
SESSION JAN-MAY 2020

## Slide 15
Multiple load/store register
LDM load multiple registers
STM store multiple registers
suffix meaning
IA increase after
IB increase before
DA decrease after
DB decrease before
15
SESSION JAN-MAY 2020
Notes: 15

## Slide 16
Addressing modes – Multiple
16
SESSION JAN-MAY 2020
CODE

## Slide 17
Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
17
SESSION JAN-MAY 2020
Notes: 17

## Slide 18
Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
18
SESSION JAN-MAY 2020
Notes: 18

## Slide 19
Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
19
SESSION JAN-MAY 2020
Notes: 19

## Slide 20
Multiple load/store register
LDM<mode> Rn, {<registers>}
IA: addr:=Rn
IB: addr:=Rn+4
DA: addr:=Rn-#<registers>*4+4
DB: addr:=Rn-#<registers>*4
For each Ri in <registers>
IB: addr:=addr+4
DB: addr:=addr-4
Ri:=M[addr]
IA: addr:=addr+4
DA: addr:=addr-4
<!>: Rn:=addr
20
SESSION JAN-MAY 2020
Notes: 20

## Slide 21
Multiple load/store register
LDMIA R0, {R1,R2,R3}
or
LDMIA R0, {R1-R3}
R1: 10
R2: 20
R3: 30
R0: 0x10
21
SESSION JAN-MAY 2020
CODE
Notes: 21

## Slide 22
Multiple load/store register
LDMIA R0!, {R1,R2,R3}
R1: 10
R2: 20
R3: 30
R0: 0x01C
22
SESSION JAN-MAY 2020
CODE
Notes: 22

## Slide 23
Multiple load/store register
LDMIB R0!, {R1,R2,R3}
R1: 20
R2: 30
R3: 40
R0: 0x01C
23
SESSION JAN-MAY 2020
CODE
Notes: 23

## Slide 24
Multiple load/store register
LDMDA R0!, {R1,R2,R3}
R1: 40
R2: 50
R3: 60
R0: 0x018
24
SESSION JAN-MAY 2020
CODE
Notes: 24

## Slide 25
Multiple load/store register
LDMDB R0!, {R1,R2,R3}
R1: 30
R2: 40
R3: 50
R0: 0x018
25
SESSION JAN-MAY 2020
CODE
Notes: 25

## Slide 26
Example
26
SESSION JAN-MAY 2020

## Slide 27
Example
LDMIA r0!, {r1-r3}
27
SESSION JAN-MAY 2020

## Slide 28
Example
LDMIB r0!, {r1-r3}
28
SESSION JAN-MAY 2020

## Slide 29
Application
Copy a block of memory
  R9: address of the source
  R10: address of the destination
  R11: end address of the source
loop: LDMIA R9!, {R0-R7}
STMIA R10!, {R0-R7}
CMP R9, R11
BNE loop
29
SESSION JAN-MAY 2020
CODE

## Slide 30
Application
Stack
(full: pointing to the last used; ascending: grow towards increasing memory addresses)
LDMFD R13!, {R2-R9} @ used for ATPCS
… @ modify R2-R9
STMFD R13!, {R2-R9}
mode | POP | =LDM | PUSH | =STM
Full ascending (FA) | LDMFA | LDMDA | STMFA | STMIB
Full descending (FD) | LDMFD | LDMIA | STMFD | STMDB
Empty ascending (EA) | LDMEA | LDMDB | STMEA | STMIA
Empty descending (ED) | LDMED | LDMIB | STMED | STMDA
30
SESSION JAN-MAY 2020

## Slide 31
Example
31
SESSION JAN-MAY 2020

## Slide 32
Q & A on Arm Instruction Set Conditional Execution & Multiple Load / Store Instructions
32
SESSION JAN-MAY 2020
Notes: 32