## Slide 1
Microprocessors & Computer Architecture
UE18CS253
Unit -1
Session – 7
ARM
Assembly Language Programming
1
Credits:
MPCA Team
Notes: 1

## Slide 2
ARM
2
Functions & Procedures
Notes: 2

## Slide 3
Functions & Procedures support in hardware
The single variant on the branch theme is the option to perform a link operation before the branch is executed. (BL)
This simply means storing the current value of R15 (PC) in R14 before the branch is taken, so that the program has some way of returning there.
  Procedure call is invoked using a BL instruction .
    Branch with link, BL instruction i.e.,
    BL subroutine
  Other processors use BSR / JSR instructions.
  Most processors implement BSR by saving the return address on the stack.
3

## Slide 4
Functions & Procedures support in hardware
ARM has no dedicated stack.
  It copies R15 into R14
If the called Routine needs to use R14 for something, it can save it on the stack explicitly.
The ARM method has the advantage that subroutines which don't need to save R14 can be called return very quickly.
The disadvantage is that all other routines have the overhead of explicitly saving R14.
To return from a subroutine, the program simply has to move R14 back into R15.
  MOV R15, R14 or MOV PC, LR
  MOVS R15, R14 or MOV PC, LR
4

## Slide 5
Functions & Procedures support in hardware
Example 1 :
A procedure to compute the statement in high level language using ARM ALP.
if (R0==R1) R2++;
BL EQUAL
SWI 0x11
EQUAL: CMP R0, R1
ADDEQ R2, R2, #1
MOV PC, LR
How to pass parameters to a procedure?
5

## Slide 6
Parameter passing to procedures
ARM normally follows the conventions.
  RO – R3 : Four argument registers in which to pass parameters.
  LR : One link register containing the return address register to return to the point of origin.
  The link stored in the Link Register LR (R14), is called the return address.
  This instruction branches to the address stored in register LR.
  Thus, returns to the calling program.
Advantages :
    Easier way to understand & to allow code to be reused.
    Allows the programmer to concentrate on just one portion of the task at a time.
    Parameters act as an interface between the procedure & the rest of the program and data, since they can pass values & return results.
6

## Slide 7
Parameter passing to procedures
Six steps to be followed in the execution of the procedure.
Put parameters in a place where the procedure can access them.
Transfer control to the procedure.
Acquire the storage resources needed for the procedure.
Perform the desired task.
Put the result value in a place where the calling program can access it.
Return control to the point of origin, since a procedure can be called from several points in a program.
7

## Slide 8
Parameter passing to procedures
Example 2 :
A procedure to compute the statement in high level language using ARM ALP.
if (R0==R1) R2++; Data in Regs. R0, R1 are parameters, Result in Reg. R2.
MOV R0, #10
MOV R1, #10
BL GREAT
SWI 0x11
GREAT: CMP R0, R1 ; comparison in the procedure
ADDEQ R2, R2, #1 ; conditional execution
MOV PC, LR ; return
How to pass parameters to a procedure?
Values 10 & 10 are passed in the registers R0 & R1
Result is passed back to the calling program through reg. R2
8
CODE

## Slide 9
Parameter passing to procedures using stack
Consider the following statement with three variables F, G & H
F = ( G + H ) => R0 = ( R1 + R2 )
; Without Procedure call.
MOV R1, #25
MOV R2, #25
MOV R0, #0
ADD R0, R1, R2 ; Register R0 (F) contains G + H
How to send parameters to a procedure through a stack & compute in the procedure ?
How are results sent back to the calling program thro’ stack?
9

## Slide 10
Parameter passing to procedures using stack
Consider the complex statement contains the five variables F, G & H ; F = ( G + H ) => R0 = ( R1 + R2 ) ;
Evaluation Using Procedure & parameters on stack.
LDR R4, =A
MOV R1, #25 ; parameter1
MOV R2, #25 ; parameter2
STMFD R13!, { R1, R2} ; parameters are PUSHed on stack.
BL LINK
STR R0, [R4] ; return value in Reg. R0.
SWI 0x11
LINK: LDMFD R13!,{ R4, R5} ; parameters are POPed from the stack
ADD R0, R4, R5 ; Result is in register R0.
MOV PC, LR
A: .WORD 0
.END
NOTE:
Result can be sent to the calling program through the stack. Left as an exercise.
10
CODE

## Slide 11
Q & A on Arm Instruction Set Functions & Procedures Instructions
11
Notes: 11