## Slide 1
Chapter 2
Memory Hierarchy Design
Computer Architecture
A Quantitative Approach, Fifth Edition
Section 2.1 Only

## Slide 2: Introduction
Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality insures that nearly all references can be found in smaller memories
  Gives the allusion of a large, fast memory being presented to the processor
Introduction

## Slide 3
Principle of locality
Temporal locality (locality in time): if an item is referenced, it will tend to be referenced again soon.
Spatial locality (locality in space): if an item is referenced, items whose addresses are close by will tend to be referenced soon.
for-loop is temporal locality
array is spatial locality
Observation: temporal locality means that we don’t put all program into memory whereas spatial locality means that we don’t put all data into memory, hence we have “Memory Hierarchy”

## Slide 4: Memory Hierarchy
Introduction

## Slide 5: Memory Performance Gap
Introduction

## Slide 6: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references
      = 409.6 GB/s!
    DRAM bandwidth is only 6% of this (25 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
Introduction

## Slide 7: Performance and Power
High-end microprocessors have >10 MB on-chip cache
  Consumes large amount of area and power budget
Introduction

## Slide 8
Q & A