## Slide 1
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 2
COMPUTER NETWORKS
Network Layer and Internet Protocol
Ashwini M Joshi (Ph.D.)
Department of Computer Science and Engineering

## Slide 3
COMPUTER NETWORKS
Chapter Goals:
Understand principles behind network layer services:
  network layer service models
  forwarding versus routing
  how a router works
  routing (path selection)
  broadcast, multicast
Instantiation, implementation in the Internet
Unit – 4 Network Layer and Internet Protocol

## Slide 4
COMPUTER NETWORKS
Unit – 4 Network Layer and Internet Protocol
4.1 Introduction
4.2 Virtual circuit and datagram networks
4.3 What’s inside a router
4.4 IP: Internet Protocol
  Datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 Routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 Routing in the Internet
  RIP
  OSPF
  BGP
4.7 Broadcast and multicast routing

## Slide 5
Network Layer and Internet Protocol
COMPUTER NETWORKS
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 6
Two key network-layer functions
COMPUTER NETWORKS
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 7
COMPUTER NETWORKS
Interplay between routing and forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 8
COMPUTER NETWORKS
Connection setup
Connection set-up can be the 3rd important function in some network architectures:
  ATM, frame relay, X.25
before datagrams flow, two end hosts and intervening routers establish virtual connection
  routers get involved
network vs transport layer connection service:
  network: between two hosts (may also involve intervening routers in case of VCs)
  transport: between two processes

## Slide 9
COMPUTER NETWORKS
Network service model
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing
Q: What service model for “channel” transporting datagrams from sender to receiver?

## Slide 10
COMPUTER NETWORKS
Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees ?

## Slide 11
COMPUTER NETWORKS
Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
Quality of Service (QoS) Guarantees ?

## Slide 12
COMPUTER NETWORKS
Ashwini M Joshi (Ph.D.)
Department of Computer Science and Engineering

## Slide 13
COMPUTER NETWORKS
Chapter 4: outline
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing

## Slide 14
COMPUTER NETWORKS
Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame

## Slide 15
COMPUTER NETWORKS
Input port functions
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric

## Slide 16
COMPUTER NETWORKS
Input port functions
line
termination
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
switch
fabric
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
(chapter 6)

## Slide 17
COMPUTER NETWORKS
Destination-based forwarding
Q: but what happens if ranges don’t divide up so nicely?
3

## Slide 18
COMPUTER NETWORKS
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 19
COMPUTER NETWORKS
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 20
COMPUTER NETWORKS
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 21
COMPUTER NETWORKS
Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 22
COMPUTER NETWORKS
Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: ~1M routing table entries in TCAM

## Slide 23
COMPUTER NETWORKS
Switching fabrics
transfer packet from input link to appropriate output link
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
R
R
R
R
(rate: NR, ideally)

## Slide 24
COMPUTER NETWORKS
Switching fabrics
bus
memory
memory
interconnection
network
three major types of switching fabrics:
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable

## Slide 25
COMPUTER NETWORKS
Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 26
COMPUTER NETWORKS
Switching via a bus
datagram from input port memory to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access routers

## Slide 27
COMPUTER NETWORKS
Switching via interconnection network
Crossbar, Clos networks, other interconnection nets initially developed to connect processors in multiprocessor
8x8 multistage switch
built from smaller-sized switches
3x3 crossbar
multistage switch: nxn switch from multiple stages of smaller switches
exploiting parallelism:
  fragment datagram into fixed length cells on entry
  switch cells through the fabric, reassemble datagram at exit
3x3 crossbar

## Slide 28
COMPUTER NETWORKS
Switching via interconnection network
scaling, using multiple switching “planes” in parallel:
  speedup, scaleup via parallelism
fabric plane 0
. . .
. . .
fabric plane 1
. . .
. . .
fabric plane 2
. . .
. . .
fabric plane 3
. . .
. . .
fabric plane 4
. . .
. . .
fabric plane 5
. . .
. . .
fabric plane 6
. . .
. . .
fabric plane 7
. . .
. . .
Cisco CRS router:
  basic unit: 8 switching planes
  each plane: 3-stage interconnection network
  up to 100’s Tbps switching capacity

## Slide 29
COMPUTER NETWORKS
Input port queuing
If switch fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward

## Slide 30
COMPUTER NETWORKS
Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate. Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
This is a really important slide
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R

## Slide 31
COMPUTER NETWORKS
Output port queuing
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!

## Slide 32
COMPUTER NETWORKS
How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gbps link: 2.5 Gbit buffer
but too much buffering can increase delays (particularly in home routers)
  long RTTs: poor performance for realtime apps, sluggish TCP response
  recall delay-based congestion control: “keep bottleneck link just full enough (busy) but no fuller”
RTT C
.
N
more recent recommendation: with N flows, buffering equal to

## Slide 33
COMPUTER NETWORKS
Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 34
COMPUTER NETWORKS
Packet Scheduling: FCFS
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
  weighted fair queueing
FCFS: packets transmitted in order of arrival to output port
also known as: First-in-first-out (FIFO)
real world examples?
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 35
COMPUTER NETWORKS
Scheduling policies: priority
Priority scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5

## Slide 36
COMPUTER NETWORKS
Scheduling policies: round robin
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn

## Slide 37
COMPUTER NETWORKS
Scheduling policies: weighted fair queueing
Weighted Fair Queuing (WFQ):
generalized Round Robin
classify
arrivals
departures
link
R
w1
w2
w3
wi
Sjwj
minimum bandwidth guarantee (per-traffic-class)
each class, i, has weight, wi, and gets weighted amount of service in each cycle:

## Slide 38
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 39
COMPUTER NETWORKS
Chapter 4: outline
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing

## Slide 40
COMPUTER NETWORKS
The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 41
COMPUTER NETWORKS
IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 42
COMPUTER NETWORKS
IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 43
COMPUTER NETWORKS
IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 44: Practise Problems
Datagram size: 3000 Bytes
MTU: 500 Bytes
Header Size: 20 Bytes

## Slide 45: Practise Problems
Datagram size: 520 Bytes
MTU: 200 Bytes
Header Size: 20 Bytes

## Slide 47
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 48
COMPUTER NETWORKS
Chapter 4: outline
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing

## Slide 49
COMPUTER NETWORKS
IP addressing: Introduction
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a device (for example, a computer or a router) to the Internet.
Address Space Notations
Classful/classless Addressing
Topics discussed in this section:
The address space of IPv4 is : 232 or 4,294,967,296.
Dotted-decimal notation and binary notation for an IPv4 address

## Slide 50
COMPUTER NETWORKS
IP addressing: Introduction
In classful addressing, the address space is divided into five classes:
A, B, C, D, and E.
Class D: multicast
Class E: reserved

## Slide 51
COMPUTER NETWORKS
IP addressing: Introduction

## Slide 52
COMPUTER NETWORKS
IP addressing: Introduction
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Solution
We replace each group of 8 bits with its equivalent decimal number (see Appendix B) and add dots for separation.

## Slide 53
COMPUTER NETWORKS
IP addressing: Introduction
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Solution
We replace each decimal number with its binary equivalent (see Appendix B).

## Slide 54
COMPUTER NETWORKS
IP addressing: Introduction
Find the error, if any, in the following IPv4 addresses.
Solution
a. There must be no leading zero (045).
b. There can be no more than four numbers.
c. Each number needs to be less than or equal to 255.
d. A mixture of binary notation and dotted-decimal notation is not allowed.

## Slide 55
COMPUTER NETWORKS
IP addressing: introduction
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 56
COMPUTER NETWORKS
IP addressing: introduction
In classful addressing, a large part of the available addresses were wasted.
Classful addressing, which is almost obsolete, is replaced with classless addressing.

## Slide 57
COMPUTER NETWORKS
IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  routers typically have multiple interfaces
  host typically has one active interface (e.g., wired Ethernet, wireless 802.11)
one IP address associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 58
COMPUTER NETWORKS
Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 59
COMPUTER NETWORKS
Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 60
COMPUTER NETWORKS
Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 61
COMPUTER NETWORKS
IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 62
COMPUTER NETWORKS
IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 63
An organization is granted the block 214.17.160.0/24. The administrator wants to create 8 subnets.
a. Find the subnet mask.
b. Find the number of addresses in each subnet.
c. Find the last addresses in first subnet.
d. Find the first addresses in last subnet.

## Slide 64
Solution:
a) log2 8 =3
Extra 1s =3 Mask: /27 (24 + 3)
b.32− 27 = 5, 2^5= 32 addresses per subnet
c. Subnet 1:
the last address, we need to write 00011111 in last byte
it is 214.17.160.00011111 = 214.17.160. 31
d.
last subnet:
214.17.160.11100000 is the last byte
So first address of last subnet is: 214.17.160.224

## Slide 65
In a block of addresses, we know the IP address of one host is 25.34.12.56/16.
What are the first address (network address) and the last address (limited broadcast address) in this block?

## Slide 66
Solution:
With the information given, the first address is found by ANDing the host address
with the mask 255.255.0.0 (/16).
Host Address: 25.34.12.56
Mask (ANDed):255.255.0.0
Network Address (First):25.34.0.0
The last address can be found by ORing the host address with the mask complement 0.0.255.255.
Host Address:25.34.12.56
Mask Complement (Ored):0.0.255.255
Last Address:25.34.255.255

## Slide 67
Find the netid and the hostid of the following IP addresses.
a. 114.34.2.8
b. 132.56.8.6
Solution:
netid: 114 hostid: 34.2.8
netid: 132.56 hostid: 8.6

## Slide 68
COMPUTER NETWORKS
Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:

## Slide 69
COMPUTER NETWORKS
Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 70
COMPUTER NETWORKS
IP addressing: how to get a block?
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes

## Slide 71
COMPUTER NETWORKS
NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 72
COMPUTER NETWORKS
NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 73
COMPUTER NETWORKS
NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 74
COMPUTER NETWORKS
NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 75
COMPUTER NETWORKS
NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  address shortage should instead be solved by IPv6

## Slide 76
COMPUTER NETWORKS
Ashwini M Joshi
Department of Computer Science and Engineering

## Slide 77
COMPUTER NETWORKS
Chapter 4: outline
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing

## Slide 78
COMPUTER NETWORKS
IPV6 Objectives
To introduce the IPv6 addressing scheme and different notations used to represent an address in this version.
To explain the three types of addressing used in IPv6: unicast, anycast, and multicast.
To show the address space in this version and how it is divided into several blocks.
To discuss some reserved blocks in the address space and their applications.
To define the global unicast address block and how it is used for unicast communication.
To discuss how three levels of hierarchy in addressing are used in IPv6 deploying the global unicast block.
To discuss autoconfiguration and renumbering of IPv6 addresses.
26.1 Introduction
26.2 Address Space Allocation
26.3 Global Unicast Addresses
26.4 Autoconfiguration
26.5 Renumbering

## Slide 79
COMPUTER NETWORKS
Introduction
An IPv6 address is 128 bits or 16 bytes (octet) long as shown in Figure. The address length in IPv6 is four times of the length address in IPv4.
Colon hexadecimal notation
Zero compression
CIDR address

## Slide 80
COMPUTER NETWORKS
Examples
Show the unabbreviated colon hex notation for the following IPv6 addresses:
a. An address with 64 0s followed by 64 1s.
b. An address with 128 0s.
c. An address with 128 1s.
d. An address with 128 alternative 1s and 0s.
Solution
a. 0000:0000:0000:0000:FFFF:FFFF:FFFF:FFFF
b. 0000:0000:0000:0000:0000:0000:0000:0000
c. FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF
d. AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA

## Slide 81
COMPUTER NETWORKS
Examples
The following shows the zero contraction version of addresses in Example 26.1 (part c and d cannot be abbreviated)
a. :: FFFF:FFFF:FFFF:FFFF
b. ::
c. FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF
d. AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA:AAAA

## Slide 82
COMPUTER NETWORKS
Examples
Show abbreviations for the following addresses:
0000:0000:FFFF:0000:0000:0000:0000:0000
b. 1234:2346:0000:0000:0000:0000:0000:1111
c. 0000:0001:0000:0000:0000:0000:1200:1000
d. 0000:0000:0000:0000:0000:FFFF:24.123.12.6
Solution
a. 0:0:FFFF::
b. 1234:2346::1111
c. 0:1::1200:1000
d. ::FFFF:24.123.12.6

## Slide 83
COMPUTER NETWORKS
Examples
Decompress the following addresses and show the complete unabbreviated IPv6 address:
a. 1111::2222
b. ::
c. 0:1::
d. AAAA:A:AA::1234
Solution
a. 1111:0000:0000:0000:0000:0000:0000:2222
b. 0000:0000:0000:0000:0000:0000:0000:0000
c. 0000:0001:0000:0000:0000:0000:0000:0000
d. AAAA:000A:00AA:0000:0000:0000:0000:1234

## Slide 84
COMPUTER NETWORKS
Address space allocation
Like the address space of IPv4, the address space of IPv6 is divided into several blocks of varying size and each block is allocated for special purpose.
Most of the blocks are still unassigned and have been left aside for future use.
To better understand the allocation and the location of each block in address space, we first divide the whole address space into eight equal ranges.
This division does not show the block allocation, but we believe it shows where each actual block is located (Shown in Figure)

## Slide 85
COMPUTER NETWORKS
Address space allocation

## Slide 86
COMPUTER NETWORKS
Address space allocation
Figure shows that only a portion of the address space can be used for global unicast communication. How many addresses are in this block?
Solution
This block occupies only one-eighth of the address spaces. To find the number of addresses, we can divide the total address space by 8 or 23 . The result is (2128)/(23) = 2125 —a huge block.

## Slide 87
COMPUTER NETWORKS
Address space allocation
Figure shows that only a portion of the address space can be used for global unicast communication.
How many addresses are in this block?
This block occupies only one-eighth of the address spaces. To find the number of addresses, we can divide the total address space by 8 or 23 . The result is (2128)/(23) = 2125 —a huge block.

## Slide 88
COMPUTER NETWORKS
Algorithm for finding the allocated blocks

## Slide 89
COMPUTER NETWORKS
Unspecified address and Loopback address
The unspecified address in IPv6 is ::/128. It should never be used as a destination address.
Loopback address
The loopback address in IPv6 is ::1/128. It should never be used as a destination address.

## Slide 90
COMPUTER NETWORKS
Compatible address, Mapped address and Unique local unicast address
Mapped address
Unique local unicast address
Compatible address

## Slide 91
COMPUTER NETWORKS
Link local address and Multicast address
Mapped address
Compatible address

## Slide 92
COMPUTER NETWORKS
Global Unicast Addresses
This block in the address space that is used for unicast (one-to-one) communication between two hosts in the Internet is called global unicast address block.
CIDR notation for the block is 2000::/3, which means that the three leftmost bits are the same for all addresses in this block (001).
The size of this block is 2125 bits, which is more than enough for the Internet expansion in the many years to come

## Slide 93
COMPUTER NETWORKS
Global Unicast Addresses
Recommended Lengths of Different Parts in Unicast Addressing
Block Assignment | Length
Global Routing Prefix (n) | 48 Bits
Subnet Identifier (128—n—m) | 16 Bits
Interface Identifier (m) | 64 Bits

## Slide 94
COMPUTER NETWORKS
Mapping for EUI-64
Mapping for Ethernet MAC

## Slide 95
COMPUTER NETWORKS
Examples
1. Find the interface identifier if the physical address in the EUI is (F5-A9-23-EF-07-14-7A-D2)16 using the format we defined for Ethernet addresses.
Solution
We only need to change the seventh bit of the first octet from 0 to 1 and change the format to colon hex notation. The result is F7A9:23EF:0714:7AD2.
2. Find the interface identifier if the Ethernet physical address is (F5-A9-23-14-7A-D2)16 using the format we defined for Ethernet addresses.
Solution
We only need to change the seventh bit of the first octet from 0 to 1, insert two octet FFFE16 and change the format to colon hex notation. The result is F7A9:23FF:FE14:7AD2 in colon hex.

## Slide 96
COMPUTER NETWORKS
Examples
An organization is assigned the block 2000:1456:2474/48. What is the CIDR notation for the blocks in the first and second subnets in this organization.
Solution
Theoretically, the first and second subnets should use the block with subnet identifier 000116 and 000216. This means that the blocks are
2000:1456:2474:0000/64
and
2000:1456:2474:0001/64.
An organization is assigned the block 2000:1456:2474/48. What is the IPv6 address of an interface in the third subnet if the IEEE physical address of the computer is (F5-A9-23-14-7A-D2)16.
Solution
The interface identifier is F7A9:23FF:FE14:7AD2 (see Example 26.12). If we add this identifier to the global prefix and the subnet identifier, we get:

## Slide 97
COMPUTER NETWORKS
Autoconfiguration
One of the interesting features of IPv6 addressing is the autoconfiguration of hosts.
As we discussed in IPv4, the host and routers are originally configured manually by the network manager.
However, the Dynamic Host Configuration Protocol, DHCP, can be used to allocate an IPv4 address to a host that joins the network.
In IPv6, DHCP protocol can still be used to allocate an IPv6 address to a host, but a host can also configure itself.

## Slide 98
COMPUTER NETWORKS
Examples
Assume a host with Ethernet address (F5-A9-23-11-9B-E2)16 has joined the network. What would be its global unicast address if the global unicast prefix of the organization is 3A21:1216:2165 and the subnet identifier is A245:1232.
Solution
The host first creates its interface identifier as
F7A9:23FF:FE11:9BE2
using the Ethernet address read from its card. The host then creates its link-local address as

## Slide 99
COMPUTER NETWORKS
Examples.. Continued
Assuming that this address is unique, the host sends a router solicitation message and receives the router advertisement message that announces the combination of global unicast prefix and the subnet identifier as 3A21:1216:2165:A245:1232. The host then appends its interface identifier to this prefix to find and store its global unicast address as:

## Slide 100
COMPUTER NETWORKS
Renumbering
To allow sites to change the service provider, Renumbering of the address prefix (n) was built into IPv6 addressing.
As we discussed before, each site is given a prefix by the service provider to which it is connected.
If the site changes the provider, the address prefix needs to be changed.
A router to which the site is connected can advertise a new prefix and let the site use the old prefix for a short time before disabling it.
In other words, during the transition period, a site has two prefixes.

## Slide 101
COMPUTER NETWORKS
IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 102
COMPUTER NETWORKS
IPv6 datagram format
Traffic class: Similar to TOS
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
Traffic class
ver
32 bits

## Slide 103
COMPUTER NETWORKS
Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 104
COMPUTER NETWORKS
Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
  tunneling used extensively in other contexts (4G/5G)

## Slide 105
COMPUTER NETWORKS
Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers

## Slide 106
COMPUTER NETWORKS
Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
IPv4 datagram
IPv6 datagram
tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4

## Slide 107
COMPUTER NETWORKS
Tunneling
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!

## Slide 108
COMPUTER NETWORKS
IPv6: adoption
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
1 https://www.google.com/intl/en/ipv6/statistics.html

## Slide 109
COMPUTER NETWORKS
IPv6: adoption
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  25 years and counting!
  think of application-level changes in last 25 years: WWW, social media, streaming media, gaming, telepresence, …
  Why?

## Slide 110
COMPUTER NETWORKS
IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 111
COMPUTER NETWORKS
DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 112
COMPUTER NETWORKS
DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 113
COMPUTER NETWORKS
DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs

## Slide 114
COMPUTER NETWORKS
DHCP: more than IP addresses
DHCP returns:
  IP address
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 115
COMPUTER NETWORKS
DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 116
COMPUTER NETWORKS
DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 117
COMPUTER NETWORKS
DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
reply
request

## Slide 118
COMPUTER NETWORKS
Ashwini M Joshi (Ph.D.)
Department of Computer Science and Engineering

## Slide 119
COMPUTER NETWORKS
Chapter 4: outline
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing

## Slide 120
COMPUTER NETWORKS
ICMP: internet control message protocol
used by hosts & routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP msgs carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 121
COMPUTER NETWORKS
Traceroute and ICMP
source sends series of UDP segments to dest
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when nth set of datagrams arrives to nth router:
  router discards datagrams
  and sends source ICMP messages (type 11, code 0)
  ICMP messages includes name of router & IP address
when ICMP messages arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 122
COMPUTER NETWORKS
Ashwini M Joshi (Ph.D.)
Department of Computer Science and Engineering

## Slide 123
COMPUTER NETWORKS
Chapter 4: outline
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing

## Slide 124
 | Distance vector | Link State
Primary principle | send larger updates , about the complete network only to neighboring routers | Send smaller updates, about the link state of neighbors, to all routers
Learning about network | Learn about network only from neighbors | Learn about network only from all routers
Building the routing table | Based on inputs from only neighbors | Based on complete database collected from all routers
Advertisement of updates | Periodically ( e.g. every 30 seconds ) | Triggered updates, only when there is a change
Distance vector v/s Link state

## Slide 125
 | Distance vector | Link State
Primary principle | send larger updates , about the complete network only to neighboring routers | Send smaller updates, about the link state of neighbors, to all routers
Learning about network | Learn about network only from neighbors | Learn about network from all routers
Building the routing table | Based on inputs from only neighbors | Based on complete database collected from all routers
Advertisement of updates | Periodically ( e.g. every 30 seconds ) | Triggered updates, only when there is a change
Distance vector v/s Link state

## Slide 126
 | Distance vector | Link State
Primary principle | send larger updates , about the complete network only to neighboring routers | Send smaller updates, about the link state of neighbors, to all routers
Learning about network | Learn about network only from neighbors | Learn about network only from all routers
Building the routing table | Based on inputs from only neighbors | Based on complete database collected from all routers
Advertisement of updates | Periodically ( e.g. every 30 seconds ) | Triggered updates, only when there is a change
Distance vector v/s Link state

## Slide 127
 | Distance vector | Link State
Primary principle | send larger updates , about the complete network only to neighboring routers | Send smaller updates, about the link state of neighbors, to all routers
Learning about network | Learn about network only from neighbors | Learn about network only from all routers
Building the routing table | Based on inputs from only neighbors | Based on complete database collected from all routers
Advertisement of updates | Periodically ( e.g. every 30 seconds ) | Triggered updates, only when there is a change
Distance vector v/s Link state

## Slide 128
 | Distance vector | Link State
Routing loops | More prone ; suffer from problems like count-to-infinity | Less prone to routing loops
Convergence ( stabilisation ) | Slow | Fast
Resources | Less CPU power and memory | More CPU power and memory required
Cost |  | More than Distance vector
Scalability |  | More scalable than distance vector
Distance vector v/s Link state

## Slide 129
 | Distance vector | Link State
Routing loops | More prone ; suffer from problems like count-to-infinity | Less prone to routing loops
Convergence ( stabilisation ) | Slow | Fast
Resources | Less CPU power and memory | More CPU power and memory required
Cost |  | More than Distance vector
Scalability |  | More scalable than distance vector
Distance vector v/s Link state

## Slide 130
 | Distance vector | Link State
Routing loops | More prone ; suffer from problems like count-to-infinity | Less prone to routing loops
Convergence ( stabilisation ) | Slow | Fast
Resources | Less CPU power and memory | More CPU power and memory required
Cost |  | More than Distance vector
Scalability |  | More scalable than distance vector
Distance vector v/s Link state

## Slide 131
 | Distance vector | Link State
Routing loops | More prone ; suffer from problems like count-to-infinity | Less prone to routing loops
Convergence ( stabilisation ) | Slow | Fast
Resources | Less CPU power and memory | More CPU power and memory required
Scalability |  | More scalable than distance vector
Distance vector v/s Link state

## Slide 132
 | Distance vector | Link State
Routing loops | More prone ; suffer from problems like count-to-infinity | Less prone to routing loops
Convergence ( stabilisation ) | Slow | Fast
Resources | Less CPU power and memory | More CPU power and memory required
Cost |  | More than Distance vector
Scalability |  | More scalable than distance vector
Distance vector v/s Link state

## Slide 133
ashwinimjoshi@pes.edu
THANK YOU
Ashwini M. Joshi
Department of Computer Science and Engineering

## Slide 134
COMPUTER NETWORKS
Summary