## Slide 1: COMMUNICATION SYSTEMS
By
Prof. Prajeesha
E&CE Dept

## Slide 2: Electronic Communication systems
A communication system is composed of following blocks

## Slide 3: Input Transducer
Source: Analog or digital
Example: Speech, music, written text
Input Transducer: Converts the message produced by a source to a form suitable for the communication system.
Example:
Speech waves  Microphone Voltage

## Slide 4: transmitter
The transmitter converts the input signal to transmitted signal suited for the transmission channel.
Basic operations in the transmitter
• Modulation
• Coding

## Slide 5: Channel
Physical medium that does the transmission
Examples: Air, wires, coaxial cable, radio wave, laser beam, fiber optic cable
Every channel introduces some amount of distortion, noise and interference

## Slide 6: Effects of the channel on the transmitted signal
• Attenuation: decreasing the signal strength;
• Distortion of the signal waveform: caused by channel characteristics (linearity, frequency response, etc.)
• Noise: contamination of random natural signals added to the transmitted signal
• Interference: contaminations of extraneous signal of human sources – machinery, power lines, digital switching circuits, etc.

## Slide 7: Receiver
Extracts message from the received signal
Operations:
    Amplification
    Demodulation
    Filtering
    Decoding
Goal: The receiver output is a scaled, possibly delayed version of the message signal (ideal transmission)
Examples: TV set, radio, web client

## Slide 8: Output Transducer
Converts electrical signal into the form desired by the system
Examples: Loudspeakers, PC

## Slide 9
One-way or simplex (SX) transmission - Transmission in one direction only.
Full-duplex (FDX) system – a system, which channel allows transmission in both directions.
Full-duplex (HDX) system – a system, which channel allows transmission in both directions but not simultaneously.

## Slide 10: Modulation
Modulation is a process of changing the carrier signal characteristics according to the message Signal.
Types of Modulation:
Continuous Modulation : AM,FM
Digital Modulation: ASK,PSK,FSK

## Slide 11: Amplitude Modulation
If the amplitude of the carrier is varied according to the message it is called as Amplitude modulation

## Slide 12: Frequency Modulation
  If the frequency of the carrier is varied according to message it is called as Frequency modulation

## Slide 13: Need for Modulation
Modulation increases the distance over which the signal can be transmitted faithfully
Modulation for efficient transmission; Modulation to overcome hardware limitation;
Modulation reduces the height of the antenna.
Modulation avoid Mixing of signals
Modulation will reduce noise and interference.
Modulation for multiplexing
Modulation helps to adjust bandwidth.

## Slide 14: Demodulation
The process of recovering the message from the modulated signal is called demodulation.
Two types of demodulation
  Coherent : systems need carrier phase information at the receiver to detect and decide what data was sent
  Non coherent : systems do not need carrier phase information

## Slide 15: Fundamental Limitations in Communications
Limitations Due to Technological Problems
• Hardware availability
• Economic factors
• International and national regulating norms

## Slide 16: Fundamental Physical Limitations
Transmission Bandwidth B.
• Limits the spectrum of the transmitted signal, i.e. the maximum speed of variation of the transmitted signal.
• The time required for transmission of a given amount of information is inversely proportional to the transmission bandwidth B.

## Slide 17: Noise
• Noise is generated in all conductors and in electronic devices as well.
• Thermal noise due to random motion of the charged particles like electrons.
• Noises generated in electronic devices: shot, flicker, popcorn, avalanche.
The noise degrades the fidelity in analog communication systems and produces errors in digital communications.
Noise generation limits the weakest transmitted signal.
Significant in long-distance communications when the signal attenuation is large.

## Slide 18
Signal-to-noise ratio
S/N = signal power / noise power
Hartley-Shannon low
The rate of information transmission cannot exceed the channel capacity
C = Blog(1+S/N)

## Slide 19: The Cellular Concept
System Design Fundamentals

## Slide 20: Introduction
Goals of a Cellular System
  High capacity
  Large coverage area
  Efficient use of limited spectrum
Large coverage area - Bell system in New York City had early mobile radio
  Single Tx, high power, and tall tower
  Low cost
  Large coverage area - Bell system in New York City had 12 simultaneous channels for 1000 square miles
  Small # users
  Poor spectrum utilization

## Slide 21: Cellular concept
  Frequency reuse pattern

## Slide 22: Cells
  Base station antennas designed to cover specific cell area
  Hexagonal cell shape assumed for planning
    simple model for easy analysis → circles leave gaps
    actual cell “footprint” is amorphous (no specific shape)
      where Tx successfully serves mobile unit
  Base station location
    cell center → omni-directional antenna (360° coverage)
      not necessarily in the exact center (can be up to R/4 from the ideal location)

## Slide 23
    cell corners → sectored or directional antennas on 3 corners with 120° coverage.
      very common
      Note that what is defined as a “corner” is somewhat flexible → a sectored antenna covers 120° of a hexagonal cell.
      So one can define a cell as having three antennas in the center or antennas at 3 corners.

## Slide 24: Cellular concept continued…
Cells labelled with the same letter use the same group of channels.
Cell Cluster: group of N cells using complete set of available channels
Many base stations, lower power, and shorter towers
Small coverage areas called “cells”
Each cell allocated a % of the total number of available channels
Nearby (adjacent) cells assigned different channel groups
  to prevent interference between neighbouring base stations and mobile users

## Slide 25
Same frequency channels may be reused by cells a “reasonable” distance away
  reused many times as long as interference between same channel (co-channel) cells is < acceptable level
As frequency reuse↑ → # possible simultaneous users↑→ # subscribers ↑→ but system cost ↑ (more towers)
To increase number of users without increasing radio frequency allocation, reduce cell sizes (more base stations) ↑→ # possible simultaneous users ↑
The cellular concept allows all mobiles to be manufactured to use the same set of freqencies
*** A fixed # of channels serves a large # of users by reusing channels in a coverage area ***

## Slide 26: Handoff Strategies
Handoff: when a mobile unit moves from one cell to another while a call is in progress, the MSC must transfer (handoff) the call to a new channel belonging to a new base station
  new voice and control channel frequencies
  very important task → often given higher priority than new call
    It is worse to drop an in-progress call than to deny a new one

## Slide 27
choose a (handoff threshold) > (minimum useable signal level)
  so there is time to switch channels before level becomes too low
  as mobile moves away from base station and toward another base station

## Slide 28: Typical handoff parameters
  Analog cellular (1st generation)
    threshold margin △ ≈ 6 to 12 dB
    total time to complete handoff ≈ 8 to 10 sec
  Digital cellular (2nd generation)
    total time to complete handoff ≈ 1 to 2 sec
    lower necessary threshold margin △ ≈ 0 to 6 dB
    enabled by mobile assisted handoff

## Slide 29
  benefits of small handoff time
    greater flexibility in handling high/low speed users
    queuing handoffs & prioritizing
    more time to “rescue” calls needing urgent handoff
    fewer dropped calls → GOS increased
  can make decisions based on a wide range of metrics other than signal strength
    such as also measure interference levels
    can have a multidimensional algorithm for making decisions

## Slide 30
  MSC dynamically decides which signal is best and then listens to that one
    Soft Handoff
    passes data from that base station on to the PSTN
  This choice of best signal can keep changing.
  Mobile user does nothing for handoffs except just transmit, MSC does all the work
  Advantage unique to CDMA systems
    As long as there are enough codes available

## Slide 31: Co-Channel Interference
Interference is the limiting factor in performance of all cellular radio systems
What are the sources of interference for a mobile receiver?
Interference is in both
  voice channels
  control channels

## Slide 32
Frequency Reuse
  Many cells in a given coverage area use the same set of channel frequencies to increase system capacity (C)
  Co-channel cells → cells that share the same set of frequencies
  VC & CC traffic in co-channel cells is an interfering source to mobiles in Several different cells

## Slide 33: Possible Solutions?
  1) Increase base station Tx power to improve radio signal reception? _
    this will also increase interference from co-channel cells by the same amount
    no net improvement
  2) Separate co-channel cells by some minimum distance to provide sufficient isolation from propagation of radio signals?
    If all cell sizes, transmit powers, and coverage patterns ≈ same → co-channel interference is independent of Tx power