## Slide 1: TRANSISTORS

## Slide 2: Invention of the Transistor
NPN
PNP
Bell Labs (1947): Bardeen, Brattain, and Shockley
Originally made of germanium
Current transistors made of doped silicon

## Slide 3: Bipolar Junction Transistor (BJT)
BJT is a three terminal device consisting of either a p type semi-conductor or n-type semi-conductor sandwiched between opposite types.
2 TYPES OF TRANSISTORS
    NPN
    PNP

## Slide 4: TYPES OF TRANSISTORS
NPN SYMBOL
PNP SYMBOL

## Slide 5: TRANSISTOR REGIONS
EMITTER
  Region to the left end
  Most heavily doped Region
  Terminal connected from this region is the emitter terminal
  Function : To supply majority charge carriers
  BASE
  Centre region
  Doping is least
  Smallest of the 3 regions
  The terminal taken out from this region is base terminal.
  Function: Controls the movement of majority charge carriers from the emitter to the collector.

## Slide 6: TRANSISTOR REGIONS Contd…..
COLLECTOR
Region to the right end
Moderately doped
Widest of the 3 regions
    (maximum power is dissipated in this region)
The terminal taken out from this region is collector terminal
Function : Collects the majority charge carriers supplied by the emitter.

## Slide 7: Transistor biasing
Transistor is made of two junctions.
EB-junction& CB-junction
Hence a transistor can be biased in 4 ways as:
  EB & CB junctions both are forward biased
  EB & CB junctions both are reverse biased
  EB junction is forward biased &CB is reverse biased
  EB junction is reverse biased &CB is forward biased
Best biasing technique is EB-Forward biased &CB-Reverse biased

## Slide 8: Transistor biasing contd….

## Slide 9: Transistor operation
With the external sources, VBE and VCB, connected as shown:
• The emitter-base junction is forward biased
• The base-collector junction is reverse biased

## Slide 10: Transistor operation
CASE 1: UNBIASED TRANSISTOR
CASE 2: EB junction is opened, CB junction is reverse biased.
CASE 3: : EB junction is forward biased with CB junction is reverse biased.

## Slide 11: Currents in a transistor
Emitter : IE = IPE + INE (largest (mA))
Base: IB = IPE + (INE – INC)- ICBO (very less(micro A))
Collector: IC = INC + ICBO (large (mA))
Emitter current is the sum of the collector and base currents:
IE = IB + IC

## Slide 12: TRANSISTOR CONFIGURATIONS
Depending on the Common terminal, there are 3 transistor configurations:
Common Base
Common Emitter
Common Collector

## Slide 13: Transistor Characteristics
The characteristics is the graph between voltage and current variations plot
Transistors characteristics are categorised as,
1.CB mode characteristics
2.CC mode characteristics
3.CE mode characteristics
In each mode of transistors characteristics, the study of its input
characteristics & output characteristics is conducted.
• Input characteristics is, the graph between Input voltage
variations and the respective changes in the input current for
the constant control by output voltage
• Output characteristics is, the graph between Output voltage
variations and the respective changes in the Output current for
the constant control by input current

## Slide 14: Common base configuration
The base is common to both input (emitter–base) and output
(collector–base) of the transistor.

## Slide 15: CB mode - Input Characteristics
Input Resistance (Rin) is the ratio of input voltage to the input current of the transistor for a constant value of output voltage.
i.e Rin = VEB/IE for a constant value of VCB
This curve shows the relationship between of input current (IE)
to input voltage (VBE) for three output voltage (VCB) levels

## Slide 16: CB mode - Output Characteristics
Output Resistance (Rout) is the ratio of output voltage to the output current of the transistor for a constant value of input current.
i.e Rout = VCB/IC for a constant value of IE

## Slide 17: OPERATING REGIONS
Active – Operating range of the amplifier.
Cutoff – The amplifier is basically off.
Saturation – The amplifier is ON

## Slide 18: CURRENT GAIN – ALPHA
The current gain ‘α’ of a transistor in CB configuration is defined as the ratio of output current (Ic) to the input current (IE )
Ideally, α is having value 1
In reality, it is between 0.95 and 0.998
α= Ic/ IE.

## Slide 19: Transistor as an amplifier

## Slide 20: Transistor characteristics in CE mode
The emitter is common to both input (base emitter) and output (collector-emitter).
The input is on the base and the output is on the collector.

## Slide 21: CE mode - Input & Output Characteristics

## Slide 22: Common-Emitter Amplifier Currents
Ideal Currents:
IE = IB + IC
IC = α IE + ICBO
Actual Currents:
IE = IB + IC
IC = β IB + (β+1) ICBO
= β IB + ICEO

## Slide 23: CURRENT GAIN – beta
The current gain ‘β’ of a transistor in CE configuration is defined as the ratio of change in collector current (Ic) to the base current (IB ).
In reality, it is between 50 and 400
β= Ic/ IB.

## Slide 25: mosfet

## Slide 26: Types of mosfet
MOSFET
Depletion Type Enhancement Type
N channel P channel N channel P channel

## Slide 27: E- type mosfet construction

## Slide 28: Basic operation of the e type mosfet

## Slide 29: e type mosfet transfer curve

## Slide 30: Mosfet symbols